1.Input

Rating input voltage

Input voltage range

Rating input current

Max input power

100~240Vac 50/60Hz

90~264Vac

3.3Arms

320W

Input:100V Output:Full load

Input:100V Output:Full load

2.Output

No load output voltage

Output voltage range

Suit with battery type

Charging current

DC44.4V 1%

DC30.0~44.4V

36V Pb-Acid battery

7.0A 7%

Charging voltage CVH

DC44.4V 1%

Floating charge voltage CVL    DC41.4V 1%

Charge-end current

Timer

1.4A20%

-

Max output power

Ripple voltage

Power LED

297.48W

530mV

Full load

Red

Power on

No battery

Finished

Error

All off

All on

All flashing

Flashing one by one

Yes

Charging LED

Charging

Shorted

Reversed

Efficiency

Yes

95%

Full load @220V

3.Environment

Operate temperature

Operate humidity

Storage temperature

Storage humidity

Cooling

-10 ~ +40

< +90%

Relative humidity

Relative humidity

-40 ~ +70

0 ~ +95%

Natural

5MM/50HZ/600S

1 meter drop test 3 times

Vibration resistance

Impact resistance

Non-operating condition

Non-operating condition

4.Mechanical

Weight

1.3Kg

Size

220X105X44MM

Refer to order

Casing only

Connector

5.Safety

Max. temperature rise

Safety approval

MTBF

ESD

< 40on casing

CB/CE/FCC

30000H

8.0KV

Hi-Pot Insulation

i/p to o/p: 3000V (1 min)

G(A)300-444067     36V 6.7A   Pb-Acid Battery Charger

Item                  Specification Remark